## Slide 1: TEAm cell-u-later
End of Term Presentation
Kevin Crean, Hudson Dye, Wyatt Hill, Davis Hobbs

## Slide 2: Agenda
Team Overview
Subsystem Progress
  Wireless Communication
  User Interface
  Onboard Processing
  Power Distribution and Management

## Slide 3: Project Overview
Project Mission: Create a data collection waystation that collects data from deployed sensor packages, computes structural health metrics, and sends the metrics through a commercial cellular network.
Project Description:
Wireless communication between the waystation and the sensors.
Onboard computing at waystation to calculate structural health metrics.
Results passed on to a host PC via commercial cellular network

## Slide 4: System Block Diagram

## Slide 5: Design Philosophy
Physical Limitations: Size and Weight
Monetary Limitations: Pricing
Ease of Implementation
ADD DIAGRAM

## Slide 6: Team organization
Project Sponsor: Austin Downey
Team Lead: Kevin Crean
Onboard Processing Subsystem: Kevin Crean
Wireless Communication: Hudson Dye
Power Distribution and Management: Davis Hobbs
User Interface: Wyatt Hill

## Slide 7: Project status: Schedule
Acquired all necessary parts to prototype entire system
Completed subsystem demonstrations
Meeting consistently at least once a week

## Slide 8: Project status: Financials
Component | Price
Botletics SIM700A-LTE-Shield (2) | $65
Micro SIM card + IoT subscription | $5
LP311P Differential Comparator (2) | $3
OKR-T-3-W12-C Buck Converter (2) | $16
SUNER BC-10 Solar Panel | $56
Talent Cell 5V/12000mAh Lithium-ion Battery | $40
SAE– Barrel Jack adapter | $10
 | $195

## Slide 9: High Level Problems
Transferring pre-packaged data to generic data files
Power Management for regulated battery voltage
Understanding new concepts
  RF Communication/Protocol

## Slide 10: Wireless Communication subsystems
Hudson Dye

## Slide 11: Block Diagram – communication focused
Notes: Please change background color of this picture to white

## Slide 12: Block Diagram – Information flow
Notes: Please change background color of this picture to white

## Slide 13: Wireless subsystems
Cellular Communication
Cellular chip + microSIM
IoT connection to user
Chip-to-Chip RF
NRF chip
Previously implemented RF connection

## Slide 14: Cellular Communication functions
Read chip & source information
  battery voltage, ID, etc.
Read wireless environment information
  registration status, RSSI, network time, etc.
Send/Receive SMS
post chip information to dweet.io
Goal: Send files to user via IoT

## Slide 15: Cellular Characterization
This slide may include evidence of functioning cellular IoT capabilities

## Slide 16: Learning Process
Custom PCB necessary to use any microcontroller except Arduino
  Use Arduino Uno for prototyping
Spent ~25 hours testing faulty chip
  Provided with free replacement extensive troubleshooting with CEO
  Will need to play catch up during Christmas for RF portion
This delayed RF communication implementation

## Slide 17: user interface (UI) Subsystem
Wyatt Hill

## Slide 18: UI Subsystem overview

## Slide 19: UI Subsystem Functions
Read Function
  Ability to read and display data from data storage
  Ability to select specific points and periods of data and read and display it from data storage.
Write Function
  Ability to write to data storage for use of the read function
  Ability to write processed data real time when requisition is given

## Slide 20: Ui Read function Experiment
The Data sheet is loaded with mock data
  First Name
  Last Name
  Country
The read function is called from UI as in normal operation
The debug window of the UI will be populated with mock data if the read function is successful

## Slide 21: UI Experimental results
2 trials with different names and countries were successful

## Slide 22: UI Subsystem Next steps
Work with Communication subsystem to achieve completion of write function.
Implement user input window for read function of UI subsystem
Integrate functions to successfully interface with local storage

## Slide 23: Onboard processing subsystem
Kevin Crean

## Slide 24: Onboard processing subsystem objective
Microcontroller receives and saves raw data to SD card.
Code will perform the structural health metrics that are requested.
Once metrics are calculated, processed data will be sent wirelessly to the user interface.

## Slide 25: Onboard processing Experiment: Read and Write SD Card
Read and Write to test file contained on SD Card
Print out Results on Serial Monitor
Serial Peripheral Interface (SPI) Protocol.

## Slide 26: Onboard processing Experiment: Mean function
Stores Data in an Array
Finds the Average Value
Running Average Function

## Slide 27: Onboard processing problems and concerns
Learning Arduino Programming Language
  Some parts taking longer than expected
Fast Fourier Transform Function
  Low Resolution that Arduino Mega 2560 R3 will be able to compute
Switching to a Raspberry Pi
  Potentially Delay Gantt Chart Schedule

## Slide 28: Onboard processing next steps
Combine and Adjust Mean Function Calculation Code with Read/Write SD Card Code
Write Fast-Fourier Transform Function
Microcontroller communication with nRF module
Using a Raspberry Pi instead of the Arduino Mega 2560 R3

## Slide 29: Power Distribution and Management (PDM) Subsystem
Davis Hobbs

## Slide 30: PDM Subsystem Overview

## Slide 31: PDM Subsystem Objectives
Power Supply
  Establish a ~5 V power source to supply the microcontroller
  High capacity with solar recharge capabilities
Power Distribution
  Establish a ~3.3V power source to supply the comms hardware
  Capable of enduring rapid changes in load
Power Management
  Signal the microcontroller when the battery is at low capacity

## Slide 32: Subsystem Hardware: Power Supply
A 5V Talent Cell Battery was selected
  Internal 5V regulator to reduce voltage ripple
  Internal battery management system allows for solar panel integration
  Sufficient capacity for 4 days of operation using data sheet values
The battery is supported by a 12 W Suner Solar Panel
  Interfaces with battery via an SAE connector
  Designed for Li Battery charging

## Slide 33: Subsystem Hardware: Power distribution
OKR buck converter supplies power to comms hardware.
  Reduces ~5V battery voltage to ~3.3V
  Up to 93% efficient power conversion
  Highly effective at responding to pulsed loads
Converter has been experimentally validated to supply loads mimicking the comms hardware

## Slide 34: Distribution System Experiment
The distribution system was given a load meant to mimic comms hardware power draw.
This load was turned on and off at 15 Hz.
The effect of dynamic loading on distribution output voltage was monitored.
High current load
Mosfet Gate Signal
Mosfet
Base Load
Buck Converter
Battery: 5 V

## Slide 35: Experimental Results
The buck converter can successfully reduce battery supply voltage
The distribution subsystem provided a max load voltage range of 3.35 – 3.14 V
  This range falls well within the 3.0 – 3.6 V range acceptable by the comms hardware.

## Slide 36: Subsystem Hardware: Power Management
The LP311P comparator was selected
  Tracks battery voltage fade
  Alerts microcontroller of low battery voltage
  Microcontroller provides signal voltage to avoid overvoltage
This subsystem was experimentally validated

## Slide 37: Power Management Experiment
The power management hardware was supplied with a 3.3 V reference signal
A power supply was used to mimic battery voltage fade
The output signal of the comparator was monitored
Buck Converter
Supply: 5 V
Test Signal
Load Resistor
Comparator

## Slide 38: Power Management Experimental Results
Demonstrated to Professor Smoak
A digital signal does change from 0 V to 5.15 V when the input falls below the reference
This validates the signal is accurate under static load conditions

## Slide 39: PDM Subsystem: next steps
The original design of the power management system did not anticipate regulated battery voltage
  Necessitates a redesign of the power management system
The solar panel’s ability to charge the battery will be tested
Distribution hardware should be integrated with the comms hardware to test functionality